## Slide 1: Model Transformations in Model-Based Systems Engineering
Chris Paredis
Associate Director Model-Based Systems Engineering Center
Georgia Tech
chris.paredis@me.gatech.edu
Model-Based Systems Engineering Center

## Slide 2: Objective
Provide enough information about model transformations so that you can envision where in your organization the use of model transformations can add value
Examples are not meant to be an exhaustive review of the state of the art but only illustrations

## Slide 3: Overview of Presentation
Background — Model Transformations
  What is a model transformation? — some simple examples
  Meta-modeling and Model transformations languages
Model Transformations in MBSE?
  A taxonomy of usage scenarios
  Examples and illustrations
How to get started?
Summary

## Slide 4: What is a Model Transformation?
Model Transformation:
Any operation on a model that produces another model
Very general:
Almost anything you “do” with a model
Our primary interest:
Automated model transformations

## Slide 5: Example: Models Evolve Over Time
(from: A Practical Guide to SysML — Friedenthal, Moore, Steiner)

## Slide 6: Example: Models Evolve Over Time
(from: A Practical Guide to SysML — Friedenthal, Moore, Steiner)
We forgot to drain the residue…

## Slide 7: Example: Models Evolve Over Time
(from: A Practical Guide to SysML — Friedenthal, Moore, Steiner)
Hmm… we could make this a continuous process

## Slide 8: Model Transformations
A SysML model is a snapshot…
How are the snapshots connected to each other?
 Model Transformations
A model transformation represents knowledge…
The more sophisticated the knowledge, the more difficult the transformation is to automate

## Slide 9: Examples of Model Transformations
Transformation
Source Model
Stage-Gate Documents
Transformation
.pdf
.html
.pptx
Endogenous Transformation
Exogenous Transformation

## Slide 10: Examples of Model Transformations
Project Management Metrics
Transformation
Simulation & Optimization
Transformation
Transformation
Source Model
Stage-Gate Documents
Transformation
.pdf
.html
.pptx

## Slide 11: Some History: Model-Driven Architecture
Platform- Independent
Model
CORBA Model
MDA Tool generates all or most of the implementation code for deployment technology selected by the developer.
Java/EJB Model
CORBA
XML/SOAP Model
Java/EJB
XML/SOAP
Other
Other Model
Map Platform Specific Model to application interfaces, code, GUI descriptors, SQL queries, etc.
(from: MDA, by R. Soley: www.omg.org/mda/mda_files/MDA-Seminar-Soley6.ppt)
PIM
PSM
Code

## Slide 12: Automated Transformations: A Closer Look…
Transformation
.pdf
.html
.pptx
Source Model
Target Model
Source Modeling Language
Target Modeling Language
modeled in
modeled in
Models must be Formal

## Slide 13: Automated Transformations: A Closer Look…
Transformation
.pdf
.html
.pptx
Source Model
Target Model
Source Modeling Language
Target Modeling Language
modeled in
modeled in
Source Meta-Model
Target Meta-Model
defined by
defined by
conforms to
Formal Syntax and Semantics

## Slide 14: Modeling Languages are also Modeled Formally
UML is defined by a meta-model
This meta-model is defined in a meta-modeling language: The MOF language (Meta-Object Facility)
How is a meta-modeling language defined?
Part of the meta-model for UML
(from: A Practical Guide to SysML — Friedenthal, Moore, Steiner)

## Slide 15: The OMG Meta-Model Infrastructure
System
conforms to
conforms to
represented by
M0
Reality
Model
M1
User Model
Meta-model
M2
UML
Meta-meta-model
M3
MOF
conforms to

## Slide 16: Model Transformation Specification
conforms to
conforms to
reads
writes
refers to
refers to
executes
(Czarnecki, K., & Hellen, S., 2006)
Source Meta-model
Transformation Specification
Target Meta-model
Source Model
Transformation Engine
Target Model

## Slide 17: Implementations of Model Transformation
Imperative
  Conventional programming tools
  Access models through API of modeling tools
  Java, Python, Ruby
Declarative
  Consist of multiple declarative model transformation rules
    Left-hand side = applicability pattern
    Right-hand side = model modification to apply
  Transformation engine automatically determines which rules to apply
  ATL, QVT, Moflon, GReAT, VIATRA2,…

## Slide 18: Generative Model Transformation for Hydraulic System
Model Transformation rules to generate systems
Generate random system alternatives by applying rules in randomized order
(Example in MOFLON)
Notes: New add rule; finds an unconnected cylinder, adds a directional valve.

## Slide 19: Generative Model Transformation for Hydraulic System
Model Transformation rules to generate systems
Generate random system alternatives by applying rules in randomized order
(Example in MOFLON)
Notes: New add rule; finds an unconnected cylinder, adds a directional valve.

## Slide 20: Decision Tree of Generation Process
Notes: I created this in Magicdraw instead of copying the one I have laid out in Moflon because I thought it was easier to read. The two are analogous.

## Slide 21: Overview of Presentation
Context — Model Transformations
  What is a model transformation? — some simple examples
  Meta-modeling and Model transformations languages
How can model transformations be useful in MBSE?
  A taxonomy of usage scenarios
  Examples and illustrations
How to get started?
Summary

## Slide 22: Taxonomy for Model Transformations in MBSE
Organized by the nature of the knowledge encoded in the transformation
  Knowledge about Views
    Take information from a model and represent it in a different (graphical) syntax
  Knowledge about Analysis
    Take a structural description of a system and generate a corresponding analysis model
  Knowledge about Synthesis
    Generate a (more detailed) structural description
From simple to sophisticated From specific to general

## Slide 23: Why are Model Transformations Important? Collaboratively Developing Complex Systems
Software
Manufacturing
Project Management
Testing
Analysis
CAD
Fuselage
Landing Gear
Engines
…
Notes: Multiple stakeholders involved in development of a complex system
Each stakeholder / group of stakeholders has a different view on the system
However, together, all stakeholders aim at achieving a common goal – e.g. developing a new jet fighter

## Slide 24: Why are Model Transformations Important? Highly Interrelated Information & Knowledge
Software
Manufacturing
Project Management
Testing
Analysis
CAD
Fuselage
Landing Gear
Engines
…
Relations /
Dependencies
Notes: Even though each stakeholder has his / her own view on the system, none of the views are completely disjunct
The artifacts produced by one stakeholder may depend in part or whole on what another stakeholder produced – e.g. CAD geometry -> aerodynamics analysis / aircraft performance, manufacturing analysis

## Slide 25: Why are Model Transformations Important? MBSE Allows for More Formal Communication
System Model
Software
Manufacturing
Project Management
Testing
Analysis
CAD
Fuselage
Landing Gear
Engines
…
Notes: Transition to model-based systems engineering enables more formal communication
Using formal models is enabler for explicitly and precisely capturing relations between the different models produced by stakeholders
What does it mean to be consistent in mbse?

## Slide 26: Why are Model Transformations Important? MBSE Allows for More Formal Communication
System Model
Software
Manufacturing
Project Management
Testing
Analysis
CAD
Fuselage
Landing Gear
Engines
…
Notes: Transition to model-based systems engineering enables more formal communication
Using formal models is enabler for explicitly and precisely capturing relations between the different models produced by stakeholders
What does it mean to be consistent in mbse?

## Slide 27: Example: Representing CAD parts in Creo as SysML Blocks in MagicDraw
(from: Manas Bajaj, InterCAX)

## Slide 28: Example: Representing Assembly Structures in Windchill as SysML part properties in MagicDraw
(from: Manas Bajaj, InterCAX)
SysML model block structure
Part structure (BOM) in PLM systems (e.g. Windchill)
Auto-generation and sync

## Slide 29: Document Generator by INCOSE SE2 team (mbse.gfse.de)

## Slide 30: Document Generator by INCOSE SE2 team (mbse.gfse.de)

## Slide 31: Document Generator by INCOSE SE2 team (mbse.gfse.de)
SysML + Profile
Transformation
DocBook XML file
XSLT Transformation
.html .pdf .docx

## Slide 32: Using DocGen at JPL
(Source: “Model Based Document and Report Generation for Systems Engineering,” Delp, Lam, Fosse, Lee)

## Slide 33: Taxonomy for Model Transformations in MBSE
Organized by the nature of the knowledge encoded in the transformation
  Knowledge about Views
    Take information from a model and represent it in a different (graphical) syntax
  Knowledge about Analysis
    Take a structural description of a system and generate a corresponding analysis model
  Knowledge about Synthesis
    Generate a (more detailed) structural description
From simple to sophisticated From specific to general

## Slide 34: Why are Model Transformations Important? MBSE Allows for More Formal Communication
System Model
Software
Manufacturing
Project Management
Testing
Analysis
CAD
Fuselage
Landing Gear
Engines
…
Notes: Transition to model-based systems engineering enables more formal communication
Using formal models is enabler for explicitly and precisely capturing relations between the different models produced by stakeholders
What does it mean to be consistent in mbse?

## Slide 35: Execute Parametric Models in ModelCenter
Syntactic transformation from parametrics to ModelCenter
Transformation
System Properties
Analysis Model
Notes: Should the models be updated automatically

## Slide 36: SysML-Modelica Transformation Specification
SysML-Modelica Transformation follows the principles
of Model-Driven Architecture (MDA)
Notes: Note: Modelica Simulation models should have relationship of “conformsTo” Modelica meta-model. Needs to be fixed.

## Slide 37
Modelica
SysML4Modelica
Bi-directional Transformation

## Slide 38: SysML4Modelica to Modelica Syntactical Mapping

## Slide 39: Transform Structure into Analysis Model

## Slide 40: Transform Structure into Analysis Model
Transformation requires deep analysis knowledge…

## Slide 41: Model Transformations for Fluid Power
Transformation Rules:
  If Cylinder in descriptive, then ModelicaCylinder in analytical
  If Pump in descriptive, then ModelicaPump and ModelicaFilter in analytical
  …
  If connection between Pump and Valve, then ModelicaConnection between ModelicaPump and ModelicaValve
  …
Not a good idea!
Too many rules…
Too specific, brittle

## Slide 42: Define Model Correspondences
Correspondence Models
Notes: Multiple levels of abstraction!!!

## Slide 43: Structure to Analysis Mapping
SysML4Modelica Analysis Model
SysML Descriptive Model
Transformation
Transformation
Modelica Model
Only 2 rules
One for components
One for connections

## Slide 44: Generation of Vehicle Analyses (Work with students B. Bailey, J. Branscomb & Ford Motor Company)
Reference model of logical vehicle architecture in SysML
Specialize the reference model into a variant for a specific vehicle program
Specify the types of analyses needed

## Slide 45: Generation of Vehicle Analyses (Work with students B. Bailey, J. Branscomb & Ford Motor Company)
Automatically generate templates for:
  Modelica (for physics-based modeling)
  Simulink (for controls)
Subsystem modeling
  SME fill in model details
  Validate subsystem models
System-level model integration
  Guaranteed compatibility
  Modelica model integrated into Simulink
Architecture in SysML
Logical Vehicle
Automated Transformation
Integrated Simulink- Modelica Model

## Slide 46: Taxonomy for Model Transformations in MBSE
Organized by the nature of the knowledge encoded in the transformation
  Knowledge about Views
    Take information from a model and represent it in a different (graphical) syntax
  Knowledge about Analysis
    Take a structural description of a system and generate a corresponding analysis model
  Knowledge about Synthesis
    Generate a (more detailed) structural description
From simple to sophisticated From specific to general

## Slide 47: Synthesis Rules
Capture heuristic synthesis knowledge: What are promising system architectures?
Difficult to create a transparent “grammar” — which architectures are covered by the grammar?
Notes: New add rule; finds an unconnected cylinder, adds a directional valve.

## Slide 48: Additional Example of Synthesis Knowledge
Variant modeling — constraint-based representation of a set of architectures (mbse.gfse.de)
F6 program at JPL: Generation and analysis of fractionated satellite systems
Transformation
Set of variations
One variant

## Slide 49: Architecture Exploration Using SysML & CPLEX (Work with former students Alek Kerzhner)
Formulate Problem in SysML
Transform to Superstructure
Transform to Introduce Behavior
Transform to Linearize
Transform to AIMMS syntax
Solve using CPLEX
Transform solutions into SysML
SE Problem
AIMMS – CPLEX
Generation of Mixed Integer Programming model through transformations
Notes: See next slides for detailed notes

## Slide 50: Overview of Presentation
Context — Model Transformations
  What is a model transformation? — some simple examples
  Meta-modeling and Model transformations languages
How can model transformations be useful in MBSE?
  A taxonomy of usage scenarios
  Examples and illustrations
How to get started?
Summary

## Slide 51: How to get started..
Imperative modeling
  Traditional programming languages: Java, Python,…
  Direct use of the APIs of SysML and Analysis tools
Declarative Model Transformation Languages
  ATL, QVT, Moflon, VIATRA2,…
  All are Eclipse based
  Integration of Model Transformation tools into current SysML tools is not well supported…

## Slide 52: Model Transformation Tools
conforms to
conforms to
reads
writes
refers to
refers to
executes
(Czarnecki, K., & Hellen, S., 2006)
Source Meta-model
Transformation Specification
Target Meta-model
Source Model
Transformation Engine
Target Model
Eclipse MMT
SysML Tool
Analysis Tool

## Slide 53: So What? Should I use Model Transformations?
It depends…
Costs
  Knowledge capture, management is expensive
  Requires “knowledge engineers” who understand how best to generalize knowledge and encode it in transformations
  Infrastructure
Benefits
  Improved consistency
  Once the knowledge has been captured, the cost of applying it is very small
  Eliminate tedious, non-value-added tasks in MBSE process

## Slide 54
Model Transformations
  Any operation on a model that produces another model
  Automated model transformations defined at meta-model level
  Model transformation tools in Eclipse
Model Transformations in MBSE
  Views: Synchronize views and maintain consistency
  Analysis: Generate analysis models
  Synthesis: Generate promising architectures
Cost-Benefit
  Identify simple MBSE tasks that are tedious and error-prone
Model-Based Systems Engineering Center
Key Take-Aways
Notes: hit the biggest payoffs!

## Slide 55
cser13.gatech.edu