## Slide 1: Using Modelica and FMI to evaluate requirements compliance early in system design
Hubertus Tummescheit, Jesse Gohl, Anh Nguyen Modelon

## Slide 2: Agenda
The Functional Mockup Interface: FMI
A Real-World Example: Active Grill Shutter Controls
Vehicle Thermal Management with Modelica
Continuous Validation of System Requirements
  Intermediate results from ITEA3 MODRIO project
Iterative Controller Development Using Rational Rhapsody & Dymola
Conclusions

## Slide 3: Modelon
Head Office
Modelon AB Lund, Sweden
Engineering Office
Modelon Deutschland GmbH Munich, Germany
Hamburg, Germany
Head Office
Modelon KK Tokyo, Japan
Head Office
Modelon, Inc. Hartford, CT
Engineering Office
Modelon, Inc. Ann Arbor, MI
Experts in solutions for model-based systems and control design
Global premier provider of FMI and Modelica based solutions for systems engineering
Global customers mostly among Fortune 500 technology companies in Aerospace and Defense, Automotive, Energy and Industrial Equipment
Representative board members for both the FMI and Modelica standards
Over 60 engineers (MSc / PhD levels) dedicated to FMI and Modelica
Real-World solutions for Systems Engineering

## Slide 4: Functional Mockup INterface
A brief overview

## Slide 5: Functional mockup interface (FMI)
Tool independent standard to support both model exchange and co-simulation of dynamic models
Origin with EU-funded MODELISAR project led and initiated by Daimler
FMI currently supported by more than 75 tools (see www.fmi-standard.org for most up to date list)
Active development as Modelica® Association project
FMI 2.0 released July 2014 with additional functionality
Endorsed by many organizations: NAFEMS/INCOSE, ProStep, GAAG

## Slide 6: FMI in a nutshell
What is FMI?
  an application programming interface and its semantics
  an xml schema that describes the model structure and capabilities
  the structure of a zip file that is used to package the model, its resources and documentation.
82 tools support in 9 categories.
Supported by ~80 tools:
0/1-D ODE Simulators
Multibody Simulators
HIL Simulators /SIL tool chains
Scientific Computation tools
Data analysis tools
Co-simulation Backplanes
Software development tools
Systems engineering tools
SDKs
Notes: We discussed the Modelica for feature design and ROM for functional fidelity design, next is the Interfaces for multiple kinds simulation design including X-in-the-loop interfaces, and also dynamics integration, steady-state simulation, optimization, robust design,…
The key is FMI. What is FMI?...
There are currently 77 tools claimed to support FMI. And we can classify them into 7 categories. We see that FMI is actually not restricted within X-in-the-loop interface but has also affect to the interoperability at feature design and fidelity design.

## Slide 7: FMI: a business model innovation
FMI-compliant tools often allow liberally licensed export of models for distribution in the organisation and to partners.
Exported FMUs most often don’t require a license from the model authoring tool.
Deployment from few simulation specialists to designers, domain specialists, control engineers
  One FMU used by many engineers (control design)
  One FMU run on many cores (robust design, V&V testing)

## Slide 8: FMI: a business model innovation
Separate the model authoring tool from the model execution tool!
Free the model unit (FMU) from license restrictions
Make the standard widely accepted: https://fmi-standard.org/tools
Increased Collaboration possibilies among typically disparate functional areas
Reduced risk & reduction in liability through better virtual verification

## Slide 9: Automated RequirEments Verification
Systems Engineering centric FMI-based workflow example: automated requirements verification for hardware and software requirements
Requirements
Formalized requirements
Executable model of requirements (e.g. FMU)
Physical plant
Model of plant
Deployable model of plant (FMU)
Software spec
Software model or prototype
Deployable model of software (FMU)
Deployable model of environment
Automate Analysis & Deploy to team!
Development of a customized workflow to allow rapid iterations of plant & software configuration

## Slide 10: Grill shutter Controller Development
Execution / automation Platform: Dymola
Other options for execution & automation:
  Matlab/Simulink
  Excel
  Python
  Any FMI execution platform
Hardware Model: Dymola/Modelica
Controller/Software development platform: IBM Rational Rhapsody

## Slide 11: Real World Example
Fuel economy is won or lost on the system level

## Slide 12: Real world example
Target: best-in-class fuel economy
Grill shutters:
Reduce aerodynamic drag
Improve fuel economy
Notes: This example is related to a real world example. An automaker (vehicle is just for show and does not reflect actual OEM) set out to develop a new car with a target for best in class fuel economy. To achieve this target, new technology (grill shutters) were added to the vehicle. The grill shutters can be closed to reduce aero drag and thus fuel consumption. However, they also affect the airflow to the cooling system and thus degrade cooling. So, along with this new technology are new control strategies for controlling the grill shutters. As requirements get cascaded, organizations use their tools to assess their systems to requirements. Many of these tools do not comprehend thermal behavior (historically many fuel consumption models ignore thermal) and thus may not pick up key interactions here. Two requirements are at odds here so we must balance them appropriately. In this particular case, the fuel consumption target was met by the team by being very aggressive with the grill shutters and their non-thermal models provided that as a good solution. Then the thermal guys see this behavior and see that the coolant is way too hot. So, they need to add fans to meet their cooling requirements. In this case, the addition of fans never made it back to the fuel consumption model (different tools, different groups, etc.). Thus, the vehicle was built with higher cost (additional fans) and also missed the fuel economy target.
We are addressing this use case for an integrated vehicle thermal management model with our libraries and our customers. We have seen this same issue several times.
The issue is not that people don’t understand that grill shutters degrade cooling. That should be obvious and it should be obvious that fans require power. However, in a world where many CAE tools where developed without multi-domain capability or with certain assumptions being made, it is easy to miss key interactions that are important as new systems/technologies are integrated or the systems become more complex.

## Slide 13: Real world example
Non-MBSE approach:
Prototype vehicle starts overheating:
Grill shutters reduce aero drag but degrade cooling
New control strategies required
Subsystem optimization resulted in addition of fans for cooling
Higher cost and missed FE target
Develop prototype
Track test prototype
Sample Vehicle!
Notes: This example is related to a real world example. An automaker (vehicle is just for show and does not reflect actual OEM) set out to develop a new car with a target for best in class fuel economy. To achieve this target, new technology (grill shutters) were added to the vehicle. The grill shutters can be closed to reduce aero drag and thus fuel consumption. However, they also affect the airflow to the cooling system and thus degrade cooling. So, along with this new technology are new control strategies for controlling the grill shutters. As requirements get cascaded, organizations use their tools to assess their systems to requirements. Many of these tools do not comprehend thermal behavior (historically many fuel consumption models ignore thermal) and thus may not pick up key interactions here. Two requirements are at odds here so we must balance them appropriately. In this particular case, the fuel consumption target was met by the team by being very aggressive with the grill shutters and their non-thermal models provided that as a good solution. Then the thermal guys see this behavior and see that the coolant is way too hot. So, they need to add fans to meet their cooling requirements. In this case, the addition of fans never made it back to the fuel consumption model (different tools, different groups, etc.). Thus, the vehicle was built with higher cost (additional fans) and also missed the fuel economy target.
We are addressing this use case for an integrated vehicle thermal management model with our libraries and our customers. We have seen this same issue several times.
The issue is not that people don’t understand that grill shutters degrade cooling. That should be obvious and it should be obvious that fans require power. However, in a world where many CAE tools where developed without multi-domain capability or with certain assumptions being made, it is easy to miss key interactions that are important as new systems/technologies are integrated or the systems become more complex.

## Slide 14: Real world example
MBSE approach:
Define requirements
Develop model
Develop test cases
Define requirement monitors
Test virtual system instead of physical prototype!
Find requirement violation – catch overheating issue early
Improve system design to also account for thermal needs
Notes: This example is related to a real world example. An automaker (vehicle is just for show and does not reflect actual OEM) set out to develop a new car with a target for best in class fuel economy. To achieve this target, new technology (grill shutters) were added to the vehicle. The grill shutters can be closed to reduce aero drag and thus fuel consumption. However, they also affect the airflow to the cooling system and thus degrade cooling. So, along with this new technology are new control strategies for controlling the grill shutters. As requirements get cascaded, organizations use their tools to assess their systems to requirements. Many of these tools do not comprehend thermal behavior (historically many fuel consumption models ignore thermal) and thus may not pick up key interactions here. Two requirements are at odds here so we must balance them appropriately. In this particular case, the fuel consumption target was met by the team by being very aggressive with the grill shutters and their non-thermal models provided that as a good solution. Then the thermal guys see this behavior and see that the coolant is way too hot. So, they need to add fans to meet their cooling requirements. In this case, the addition of fans never made it back to the fuel consumption model (different tools, different groups, etc.). Thus, the vehicle was built with higher cost (additional fans) and also missed the fuel economy target.
We are addressing this use case for an integrated vehicle thermal management model with our libraries and our customers. We have seen this same issue several times.
The issue is not that people don’t understand that grill shutters degrade cooling. That should be obvious and it should be obvious that fans require power. However, in a world where many CAE tools where developed without multi-domain capability or with certain assumptions being made, it is easy to miss key interactions that are important as new systems/technologies are integrated or the systems become more complex.

## Slide 15: Vehicle Thermal ManagEment model
Overview

## Slide 16: Integrated Vehicle Thermal management (VTM) model
Integrated model for fuel economy and vehicle thermal management
  Vehicle model with loads and losses
  Vehicle heat loads (engine, friction, transmission)
  Lumped engine thermal model
  Coolant and oil circuits with possible additions of other thermal fluid circuits
  Drive cycles (speed, grade, wind, etc.)
  Airflow effects
  Key vehicle and thermal controls (fan, grill, etc.)
Notes: This list is just a description of the type of model needed to assess this kind of problem. We have demo models like this and are working with customers to develop their specific models. Our libraries fully support this kind of modeling (simplified VDL for vehicle modeling, Liquid Cooling, Heat Exchanger, Engine Dynamics, etc.).

## Slide 17: Modelon libraries
Multi-domain physical model libraries in Modelica
Libraries developed by Modelon domain experts leveraging industrial experience and consulting projects

## Slide 18: VTM System model
Thermal
Mechanical
Electrical
Coolant
Air
Notes: Here is a picture of a top level demo model for VTM. The various interactions are shown in the upper right hand color and correspond to the connection colors. We use the same driver and vehicle model architecture from VDL to leverage all that work and to also allow scalable vehicle model implementations. The model includes a simple representation of the heat exchanger stack from LCL. I can provide pictures of any other subsystems that you might want to show.

## Slide 19: Thermal system modeling
Air Flow
Coolant Circuit
Heat from vehicle systems enters coolant fluid
Coolant

## Slide 20: Driver and drive cycles
Boundary conditions define test case conditions:
Road grade and surface
Ambient air (temperature, pressure, wind speed, etc.)
Desired vehicle speed profile (drive cycle)
Ambient
Road
Drive Cycle
Notes: This slide just shows how the vehicle model also includes the driver and the drive cycle. This slide may not be all that interesting if you need to reduce the number of slides. Again, we utilize VDL here but just use simplified models that are typical for drive cycle work.

## Slide 21: Typical Drive cycle results
Notes: This slide shows typical drive cycle fuel consumption results (vehicle speed, engine torque, engine speed, and fuel consumed). Note that these results are from a demo model and they do not represent any actual vehicle.

## Slide 22: Typical Drive cycle results (thermal)
Fan speed is low
When vehicle is fast
Thermostat opens
As engine warms up
Temperature can only be exceeded for at most X seconds
Notes: This slide shows results from the same sim but focusing on the thermal side. Here we show coolant and oil temp, thermostat opening for the coolant, fan speed based on the fan controller, and the air temperatures in the HX stack (there is no capacitance on the air side so you see some changes reflected instantly in the temperatures). The drop in coolant and oil temps just before 1200s is due to the fan being commanded on. These control strategies are very simple and just for demo purposes.
Note, I removed the old slide as it was not as illustrative and actually came from a different sim thus there was no alignment with the previous results. My bad.

## Slide 23: Requirements Validation
Continuous feedback on compliance of requirements

## Slide 24: Requirements Validation
Translate to Executables
MBSE approach:
Stakeholder Requirements
Design Requirements
All Pass?
Test Cases
Requirements Monitors
Validator Models
Batch Execution
Result Report
Done
Modify:
Reqs
System
Model
Virtual System
Real System
Executable
Environment
Yes
Requirements
Manager
No
These exercise the system dynamics.
Combining a test case with one or more monitors allows requirements to be verified.
The complete set of executable validator models can be tested automatically.
Complete
Coverage?
When requirements are not met, modifications can be made to the system, model or even the requirements.
These are the executable checks to verify the requirements are met.
These are usually high level, not always easily testable.
Specifying the requirements in a standard way opens the possibility to automatically generate the executable monitors.
The requirements manager should be able to verify that all requirements will be tested by the set of validator models.
The report shows a summary overview of the pass/fail results.
Formalized
Requirements
These are low level and testable. When possible also specified in an open standard language.

## Slide 25: Automated Requirements Validation
Translate to Executables
MBSE approach:
Stakeholder Requirements
Design Requirements
All Pass?
Test Cases
Requirements Monitors
Validator Models
Batch Execution
Result Report
Done
Modify:
Reqs
System
Model
Virtual System
Real System
Executable
Environment
Yes
Requirements
Manager
No
Complete
Coverage?
Formalized
Requirements
Degree of
Automation?

## Slide 26: Requirements Management
Stakeholder Requirements
Design Requirements
Requirements
Manager
Requirements management tools
  IBM DOORS/DOORS NG
Requirements quality tools
  Requirements Quality Suite from The Reuse Company
Requirements traceability
  IBM Requisite Pro, integration with ClearQuest for testing, ..
  Reqtify (Dassault Systèmes), links Modelica code to req. in DOORS
Requirements formalization?
Testing of requirements against system model?
Continuous Integration tools to repeat tests for every change to the system?

## Slide 27: Executable Requirements
Translate to Executables
MBSE approach:
Stakeholder Requirements
Design Requirements
All Pass?
Test Cases
Requirements Monitors
Validator Models
Batch Execution
Result Report
Done
Modify:
Reqs
System
Model
Virtual System
Real System
Executable
Environment
Yes
Requirements
Manager
No
Complete
Coverage?
Formalized
Requirements
Focus on this part
Notes: This example is related to a real world example. An automaker (vehicle is just for show and does not reflect actual OEM) set out to develop a new car with a target for best in class fuel economy. To achieve this target, new technology (grill shutters) were added to the vehicle. The grill shutters can be closed to reduce aero drag and thus fuel consumption. However, they also affect the airflow to the cooling system and thus degrade cooling. So, along with this new technology are new control strategies for controlling the grill shutters. As requirements get cascaded, organizations use their tools to assess their systems to requirements. Many of these tools do not comprehend thermal behavior (historically many fuel consumption models ignore thermal) and thus may not pick up key interactions here. Two requirements are at odds here so we must balance them appropriately. In this particular case, the fuel consumption target was met by the team by being very aggressive with the grill shutters and their non-thermal models provided that as a good solution. Then the thermal guys see this behavior and see that the coolant is way too hot. So, they need to add fans to meet their cooling requirements. In this case, the addition of fans never made it back to the fuel consumption model (different tools, different groups, etc.). Thus, the vehicle was built with higher cost (additional fans) and also missed the fuel economy target.
We are addressing this use case for an integrated vehicle thermal management model with our libraries and our customers. We have seen this same issue several times.
The issue is not that people don’t understand that grill shutters degrade cooling. That should be obvious and it should be obvious that fans require power. However, in a world where many CAE tools where developed without multi-domain capability or with certain assumptions being made, it is easy to miss key interactions that are important as new systems/technologies are integrated or the systems become more complex.

## Slide 28: Current Research, itea3 (EU)
ITEA3 Project:
  Model Driven Physical Systems Operation
WP: Define requirements formally and check them automatically whenever a Modelica system model is simulated
Example
„Pumps should not cavitate when they are operating“ (p(t) ≥ pcav if operating) → Define formally + associate conveniently to all pumps + check automatically + report issues automatically
Otter et al: Formal Requirements Modeling for Simulation-Based Verification, Modelica’2015
State of the art
Not practical (impossible) with available Model Checkers since requirements depend on the numerical solution of Differential-Algebraic Equations (DAE).
Limited tool support for connecting „textual requirements“ with simulation models (e.g. Simulink with Validation & Verification toolbox + IBM DOORS; 3DExperience with Reqtify + Dymola, ...).
Research languages + tools (e.g. ModelicaML from Airbus Innov./LiU).
Notes: Skip details!

## Slide 29: MODRIO view of Requirements Validation
Natural language:
„Pumps should not cavitate when they are operating“
FORM_L (formal language developed by N. Thuy, EDF) required property R2 = { P in Pumps | during P.InOperation check not P.Cavitate };
1. Define requirements formally
2. Design Architecture (e.g. with SysML)
3. Provide Behavioral Models to evaluate design (Modelica)
4. Associate requirements and architecture with behavioral models
5. Verify Behavior
Otter et al: Formal Requirements Modeling for Simulation-Based Verification, Modelica’2015
Notes: Fly over quickly

## Slide 30: Prototype Implementation
Modelica extension to express requirements (under development)
FORM-L-inspired Modelica library, based on 3-valued logic: Satisfied, Undecided, Violated
Large Library of pre-defined requirement structures
 Executable and formal model of requirements, in Modelica language
(x,y) coordinates of input must stay within closed polygon (output: closest distance to polygon + property)

## Slide 31: Grill shutter controller
Development Cycle

## Slide 32: Simple Grill Shutter Controller
Initial bang-bang controller with hysteresis
Close the shutters when the vehicle speed exceeds the closing threshold
Open the shutters when the vehicle speed is below the opening threshold
Close
Close
Open
Open

## Slide 33: Simple Grill Shutter Controller
Implementation as statechart with two states
Entry actions completely open and close grill shutters
Notes: Optional remove if high-level view available

## Slide 34: Simple Grill Shutter Controller
Statechart transitions
Transition condition (guard) based on vehicle speed thresholds
Default transition to the open state

## Slide 35: Simple Grill Shutter Controller
Generate FMU
Notes: Optional remove if high-level view available

## Slide 36: Simple Grill Shutter Controller
Import FMU to the execution platform
FMU is imported and inserted into a model
Notes: Optional remove if high-level view available

## Slide 37: Thermal Management requirements
Monitors for requirements compliance checking

## Slide 38: requirements document

## Slide 39: Test cases
Test cases exercise system (or parts of system) under various operating conditions
Test cases exercise system (or parts of system) under various operating conditions
Adding test cases can improve coverage

## Slide 40: requirements monitors
Monitors used to check pass/fail status of requirements from test cases

## Slide 41: requirements monitors
Monitors from the new Modelica Requirements library (Otter et al., 2015)
Checks the conditions of the requirement
Reports pass, fail, or undecided
Constructed from standard blocks from the Requirements library
Monitors can be collected in one submodel, and be compiled into an FMU as well
M. Otter, N. Thuy, D. Bouskela, L. Buffoni, H. Elmqvist, P. Fritzson, A. Garro, A. Jardin, H. Olsson, M. Payelleville,
W. Schamai, E. Thomas, AND A. Tundis. Formal Requirements Modeling for Simulation-Based Verification. Proceedings of the 11th International Modelica Conference, Paris, France, September 21-23., pp. 625-635 2015. http://www.ep.liu.se/ecp/118/067/ecp15118625.pdf

## Slide 42: requirements monitors
Monitors added to test cases – in this case a unit test of the simple controller
Requirements violated (0 of 2):
None
Requirements untested (0 of 2):
None
Requirements satisfied (2 of 2):
(checkReq3.requirement): Grill shutter opened below 15 m/s
(checkReq4.requirement): Grill shutter closed above 18 m/s
Overall pass or fail report
Vehicle Velocity [m/s]
Grill Command [1=open, 0=closed]
Vehicle Velocity
Grill Command

## Slide 43: Controller performance
Simple Grill Shutter Controller

## Slide 44: Controller performance
Baseline system without grill shutters
Null controller holds grill shutters in wide open position
Vehicle runs the US06 drive cycle
Vehicle Velocity [m/s]
Notes: Move fast!

## Slide 45: Controller performance
Baseline system without grill shutters
Fuel Economy [mpg]
Engine Speed [RPM]
Coolant Temp [°C]
Fan Speed [RPM]
Vehicle Speed [m/s]
-------- 100.0 % of US06_no_shutters requirements are satisfied -------------
Requirements violated (0 of 3):
None
Requirements untested (0 of 3):
None
Requirements satisfied (3 of 3):
(checkReq1_1.requirement): Coolant temperature must not exceed 368.15K for longer than 20 seconds
(checkReq2_1.requirement): Coolant temperature shall not exceed 371.15K
(checkReq3_1.requirement): Grill shutter opened below 15 m/s
Notes: Baseline system fulfills requirements, but at fuel economy that can be improved

## Slide 46: Controller performance
Replace grill null position controller with statechart based bang-bang control logic as an FMU from Rhapsody
Vehicle Velocity [m/s]
Repeat the US06 drive cycle

## Slide 47: Controller performance
System with simple grill shutters
Fuel Economy [mpg]
Engine Speed [RPM]
Coolant Temp [°C]
Fan Speed [RPM]
Vehicle Speed [m/s]
-------- 50.0 % of US06_FMU_simpleGC requirements are satisfied -------------
Requirements violated (2 of 4):
(checkReq1_1.requirement at 86.3981 s): Coolant temperature must not exceed 368.15K for longer than 20 seconds
(checkReq2_1.requirement at 111.523 s): Coolant temperature shall not exceed 371.15K
Requirements untested (0 of 4):
None
Requirements satisfied (2 of 4):
(checkReq3_1.requirement): Grill shutter opened below 15 m/s
(checkReq4_1.requirement): Grill shutter closed above 18 m/s
Failed thermal requirements
In addition to failed thermal requirements, fuel economy actually decreased!
Fuel Economy [mpg]
Temperature exceeds 95°C for more than 20 seconds
Temperature exceeds 98°C

## Slide 48: Controller performance
System with simple grill shutters
Fuel Economy [mpg]
Engine Speed [RPM]
Coolant Temp [°C]
Fan Speed [RPM]
Vehicle Speed [m/s]
Closed grill shutters reduces air flow through the stack. Compensated for by increased the fan speed, draws more electrical power from the alternator… and ultimately the engine.

## Slide 49: Improved controller design

## Slide 50: Improved controller design
System with simple grill shutters
Improved controller state chart
Additional inputs to account for system temperatures

## Slide 51: Improved controller design
System with simple grill shutters
Improved controller statechart
Additional attributes to tune improved logic

## Slide 52: Improved controller design
System with simple grill shutters
Improved controller statechart
Additional states to organize improved logic

## Slide 53: Improved controller design
System with simple grill shutters
Improved controller statechart
Controller includes a PID controller
Continuously modulate the grill position between open and closed
Measured signal is weighted average of stack fluid temperatures
Proportional
Integral
Derivative

## Slide 54: Controller performance
Improved Grill Shutter Controller

## Slide 55: Controller performance
Replace the simple bang-bang control logic with the improved controller as an FMU from Rhapsody
Repeat the US06 drive cycle
Vehicle Velocity [m/s]

## Slide 56: Controller performance
System with improved grill controller
Fuel Economy [mpg]
Engine Speed [RPM]
Coolant Temp [°C]
Fan Speed [RPM]
Vehicle Speed [m/s]
-------- 100.0 % of US06_FMU_advancedGC requirements are satisfied -------------
Requirements violated (0 of 3):
None
Requirements untested (0 of 3):
None
Requirements satisfied (3 of 3):
(checkReq1_1.requirement): Coolant temperature must not exceed 368.15K for longer than 20 seconds
(checkReq2_1.requirement): Coolant temperature shall not exceed 371.15K
(checkReq3_1.requirement): Grill shutter opened below 15 m/s
Requirements now pass
Fuel economy improved, also over baseline
Fuel Economy [mpg]

## Slide 57: Summary & Conclusions
FMI simplifies tool connectivity and allows more efficient work flows & processes
FMI enables true MBSE, with executable models
Requirements monitors allow to check requirements compliance continuously during development
Process automation is key to integrate the requirements validation with MBD.
Notes: To 2: it really matters that FMI integrates EXITING tools, leveraging investments already made.

## Slide 58: Future Work
Further integration with IBM tool suite for fully automated traceability
Complete automation of requirements validation process
… much more progress on tools is needed to have a coherent work flow from
  stakeholder requirements to
  formal requirements and finally
  fully automated requirements validation.

## Slide 59
ALL CONNECTED!

## Slide 60: For more information:
info@modelon.com, +1 (860) 987 8900

## Slide 61: FMI advantage
Same model – different applications

## Slide 62: Participants